# Customer name: JSC «Riga Electric Machine Building Works»

(AS «Rīgas elektromašīnbūves rūpnīca»)

Legal adress: Ganību dambis 53, Rīga, Latvija, LV-1005

Contact personVladimir Malgin, Manufacturing manager

Contact phone: + 371 27000891

e-mail: vladimir.malgin@rer.lv; dt@rer.lv

# Requirements specification for painting chamber with dry filters

# Technical specifications

| № | Parameter | Requirements |
| --- | --- | --- |
| 1. | Chamber (booth) | For painting with liquid paints and varnishes. Pass through type. With dry filters. Must have an electrical control panel. |
| 2 | Paint booth requirements | Must be manufactured in accordance with ATEX (Zone 2) requirements. The surface of the chamber is resistant to corrosion. Must be made of corrosion-resistant material |
| 3 | Requirements for the control panel of the paint booth | Must be manufactured in accordance with ATEX (Zone 2) requirements. There should be an alarm (visual, audible) to control the dust content of the filter. Automatic shutdown of the spray gun in case of emergency. |
| 4 | Ventilation requirements | The exhaust ventilation must have a system of air filtration from paint dust and ensure maximum air purification. The exhaust ventilation must be equipped with an ATEX centrifugal explosion-proof fan with low noise load. |
| 5 | Requirements for the light source in the work area | Illumination not less than 750 lux; Explosion-proof lamps in accordance with ATEX requirements. |
| 6 | Chamber noise level | No more than 75 dB |
| 7 | Overall dimensions of the painted product | Width: 1200mm Length: 1200mm Height: 950 mm |
| 8 | Weight of the product to be painted, no more than | 1650 kg |
| 9. | Chamber overall dimensions, not less than | Width: 1400mm Length: 3000mm Height: 3000 mm |
| 10. | Safety requirements | The chamber (cabin) must comply with the EU standards for fire and electrical safety. |
| 11. | Documentation | The set of documentation should include instructions for the operation and maintenance of equipment, a repair manual with a list of names and coding of quickly worn replacement parts and assemblies, electrical diagram. Language of technical documentation – Latvian and Russian. |
| 12 | The warranty | The warranty period is not less than 12 months. |